## Slide 1: XChange: A Market-based Approach to Scalable Dynamic Multi-resource Allocation in Multicore Architectures
Xiaodong Wang
José F. Martínez
Computer Systems Lab
Cornell University
Notes: Feb. 9, 13:30-14:45

## Slide 3: Shared inter-core resources
Haswell’s Floorplan
Motivation • Prior Art
Source: Intel
Shared cache
Shared
memory pins
Shared
power budget
Notes: Designing chip multiprocessors (CMPs) that scale to more than tens or hundreds of cores is an important goal for the upcoming technology generations.
A challenge to scalability is the fact that these cores will inevitably share hardware resources, whether it be the chip’s power budget, last-level cache, off-chip memory bandwidth, shared processing elements, etc.
Allowing cores to freely contend for shared resources is historically been proven to affect the system performance negatively. Therefore, allocating resources intelligently among cores is key to achieving good behavior.

## Slide 4: Coordinated resource allocation
Global allocation space very large
  Exponentially increasing with the number of cores, the number of resources, and the granularity of resources
  Hill climbing unlikely to scale gracefully
(*) art and twolf share 16
cache ways and 20W
power: ~600 points
Motivation • Prior Art • Markets
Notes: In the past a few years, researchers have found that coordinated resource allocation can greatly improve system performance compared against unmanaged and uncoordinated resource allocation.
Let’s take a look at a simple example – a resource allocation problem in a 2-core CMP. These two cores are sharing two on-chip resources, …, with each core running one SPEC benchmark. This graph shows the system throughput, i.e., the weighted speedup, of all possible resource allocation combinations. As we can see, such allocation space is not trivial.
Uncoordinated resource allocation generally doesn’t search the space effectively, and the resulting allocation are often far from optimal.
However, evaluating all possible allocation combinations are prohibitive, because even in this simple problem, we’re having 600 allocation points, and this number ….

## Slide 5: Coordinated resource allocation
Global allocation space very large
  Exponentially increasing with the number of cores, the number of resources, and the granularity of resources
  Hill climbing unlikely to scale gracefully
Performance-resource relationship not trivial
  Not even convex for some resources (e.g., cache)
  Phase changes
Balance between system throughput and fairness
Motivation • Prior Art • Markets

## Slide 6: Real-life cue: market-like behavior
Compromise global optimality for simplicity
  Calculate global optimum is very expensive
  Optimal outcome is not practical
  Simple, distributed mechanisms can be reasonably good
Source: Wikipedia
Prior Art • Markets • Simple Market
Notes: Facing all these challenges, we’re inspired by a real life problem: traffic regulations. Thousands of cars, multiple routes …..
What people does is to set up a general framework: build the road, set up toll both, traffic signs, etc.
This type of problems with distributed solution exists, can be abstracted as a market, where given a set of general market constraints, players operates to pursue their own benefit, and the market will end up an outcome that everyone is reasonably happy.

## Slide 7: A market-based approach
Central idea: Pricing CMP resources
  Every resource is assigned a price
  Reflects supply and demand relationship
Market players (cores)
  Have finite budgets to purchase resources in the system
  Try to maximize their own utility regardless of others
  Price-takers: no monopolistic behavior
Market equilibrium
  Prices are such that supply = demand
  Our approach: Dynamic price discovery
Prior Art • Markets • Simple Market
Notes: We propose to treat the CMP resource allocation problem
(rest same as before)

## Slide 8: Strong ally: first welfare theorem
First welfare theorem
  Competitive market equilibrium is Pareto optimal, if players have monotonic increasing utilities
Pareto optimality
  An allocation is Pareto optimal if there is no way to reallocate goods so that someone is made better off without making someone else worse off
  Caveat: Not “perfect world” by itself!
Prior Art • Markets • Simple Market
Notes: one of the most powerful, and ironcally perhaps the least constraint theory is
caveat: pareto optimality is the best market can do, which does not guarantee global optimality
in the last page, we argue to compromise global optimality for simplicity

## Slide 9: Dynamic price discovery
Market side
  How to set prices to satisfy demand from cores?
Player side (cores)
  What are my preferences (utility function)?
  How do I bid to maximize my utility?
Set initial
resource prices
Players bid
independently
New prices
computed
Prices not
converge
Resources
allocated
converge
Prior Art • Markets • Simple Market
Notes: Don't say "we propose dynamic..", ---> propose to use dynamic

## Slide 10: First take: a simple market
Market side: proportional pricing [Kelly, ETT 1997]
Player side: linear utility function
  Find preferences: Sparse off- and/or on-line profiling
  Bidding strategy: [Wu and Zhang, STOC 2007]
Markets • Simple Market • A Heuristic Approach
Notes: On the market side, we want to price the resources based on the demand.
On the player side, I want to place the bids that I want most. In order to do this, I need to build a utility function.
as a first take, we adopt a simple player model, the simplest model? which assumes all the players have linear utility functions. Wu and Zhang in 2007 have proposed a bidding strategy for such player model, which provides some interesting features such as fast convergence and game-theoretic fairness.

## Slide 11: First take: a simple market
Market side: proportional pricing [F. Kelly]
Player side: linear utility function
  Find preferences: Sparse off- and/or on-line profiling
  Bidding strategy: [Wu and Zhang 2007]
Good news: Very fast convergence
Bad news: Results not that great
Chart: mcf
| 1-way | 2-way | 3-way | 4-way | 6-way | 8-way | 12-way | 16-way
 | 0.049932 | 0.049964 | 0.049975 | 0.049978 | 0.049995 | 0.049997 | 0.1998 | 0.20644
Markets • Simple Market • A Heuristic Approach
Notes: On the player side, as a first take, we adopt a simple player model, the simplest model? which assumes all the players have linear utility functions. Wu and Zhang in 2007 have proposed a bidding strategy for such player model, which provides some interesting features such as fast convergence and game-theoretic fairness.
There are two ways to go from here: explore more sophisicated analytical model to fit the application behavior. But there are two problems: difficult to get one function which fits everything; good market theory enjoyed by simple utility disappears
alternatively, we could turn to architectural heuristics. In fact, our community is doing pretty well there, especially in terms of model application behavior, we have

## Slide 12: A heuristic player model
Separate memory and compute phases
  Memory phase: cache capacity, memory bandwidth, etc.
  Compute phase: power budget, ROB, FUs, etc
We focus on allocating cache capacity and power budget in this paper
  Market framework can be applied to any other resources if an accurate utility model is built
Simple Market • A Heuristic Approach • Wealth Redistribution
Notes: This is how we do in the paper.

## Slide 13: A heuristic player model
Memory phase
  Combine Miftakhutdinov1 and UMON2
[1] Miftakhutdinov et al, MICRO 2012
[2] Qureshi and Patt, MICRO 2006
marginal utility
A1A2
# hits A1
# misses A1
# hits A2
# misses A2
Perf. counters
# hits
# misses
th
tm
Length of
mem. phase
MLP
length A1
length A2
th
tm
th
tm
Assume MLP constant
Simple Market • A Heuristic Approach • Wealth Redistribution
Notes: Ultimately, we want to see how much benefit we get from allocation A1 to A2. On memory, this is to calculate the marginal utiltiy of A1 to A2

## Slide 14: A heuristic player model
Memory phase
  Combine Miftakhutdinov1 and UMON2
Compute phase
  Linear relationship between compute phase and frequency
  Cubic relationship between power and frequency
Simple Market • A Heuristic Approach • Wealth Redistribution
[1] Miftakhutdinov et al, MICRO 2012
[2] Qureshi and Patt, MICRO 2006

## Slide 15: A heuristic bidding strategy
Local hill-climbing
  All cores search through their utility function concurrently
Simple Market • A Heuristic Approach • Wealth Redistribution
Notes: We propose to search a local hill climbing which is local to all the cores. That means, all cores search through their utility function concurrently.

## Slide 16: Wealth redistribution
Budget assignment depends on the definition of optimality
  Fairness-oriented: Give same budget to everyone
  Performance-oriented: Assigning budgets in proportional to the performance gap between minimum and maximum allocation
A Heuristic Approach • Wealth Redistribution • Design Issues
Notes: So far, we only talk about each market player has a finite amount of budget to purchase resources, but how exactly the budget assigned to each individual? The answer is, it depends on the definition of system optimality. A straight forward approach is to give the same budget to everyone. In this way, each player will have the same purchasing power in the market, leading to a fair system. However, we find that this may not be efficient in terms of system throughput.
By utilizing the player model already described, we estimate the budget in proportional to the performance difference between minimum and maximum allocation
Fair budget allocation may not be the best option, if maximizing throughput is what we’re after.
When you’re going after the throughput, this may not be the best option.

## Slide 17: Design issues
Convergence
  Detected through price fluctuation (<1%)
  Fall-back mechanism after 30 iterations
    Players quickly decide whether they prefer the current allocation or equal share
Bankruptcy
Wealth Redistribution • Practical Issues • Evaluation
Notes: The paper covers some interesting issues such as bankruptcy of players.

## Slide 18: wait—what about theoretical guarantees?
Pretty much out of the window
  Utility function approximation at best
    Based on architecture heuristics
  Bidding search not exhaustive
  Predictive: past history = future performance
Nevertheless, reason for optimism
  Plenty of real-life examples that just work
  Utility models captures application behavior well
  First welfare theorem has weak conditions
  We have reasonable fallback mechanism
Wealth Redistribution • Practical Issues • Evaluation
Notes: Before going into evaluation section, let’s stop here and remember something we mention before.
Is this bound by theoretic guarantee? No. We intentionally use heuristics to avoid complex or inaccurate analytic model. Also we have fall-back plan. How it works? Let’s see evaluation section.
However, there are reasons for optimism. Recall that the first welfare theorem has very weak conditions: basically it requires that player’s utility is monotonic, and players bid optimally. In our study, application’s utility is monotonic, because an application will not be unhappier if it’s given more cache or power. Although hill climbing cannot guarantee optimal bids, prior studies prove it works at small scale. Also the heuristic player model is accurate.
Plenty of real-life examples that operate like markets and just work.

## Slide 19: Experimental setup
Simulation setup
  4 GHz 4-way OoO core, 32 kB i/d L1
  8- and 64-core CMP
  512kB L2, 10W per core as equal-share
  DDR3-1600 channels, 4 ranks ea., 8 banks/rank
Performance analysis
  Mix of SPEC2000 and SPEC2006 multi-programed workloads
Comparison to state-of-the-art resource allocation
Practical Issues • Evaluations • Conclusions
Notes: Partition L2 cache based on cache ways. Essentially, other cache allocation techniques, such as z-cache, vantage essentially mimic high associativity with limited physical cache ways. There is no fundamental reason that we cannot use it.
not really a limitation: essentially z-cache does the same thing
640W thing: IBM Power8 12 core: 200-250W @ 22nm
Intel Haswell: 155W@ 22nm
The results doesn’t depend on the absolute number.
The actual cache partition is orthogonal to our proposal.

## Slide 20: System throughput (weighted speedup)
13.62%
18.30%
Global hill climbing,
Chen and John, ICS 2011
Resource elasticity fairness,
Zahedi and Lee, ASPLOS 2014
Practical Issues • Evaluations • Conclusions
Notes: In the next two slides, we will show the quality of the allocation of competing mechanism.
Here, we don’t factor in the cost of actually running the allocation algorithm. Later, when we show the actual allocation overhead, the results are even more promising compared against state-of-art allocation.
These are the performance results without taking into account of the overhead to calculate the allocation, in other words, we’re looking into the performance effect the quality of the allocation.
Once we factor in the quality, the potential of our approach is amplified, and we’ll show later.
Twice as good: remember this is w/o overheads factor in, and when it’s factor in
When the overhead are factor in
Is **even** more promising than GHC

## Slide 21: System fairness (maxmin slowdown)
2.24
2.88
3.23
Practical Issues • Evaluations • Conclusions
Notes: slowdown ratio: the gap between the apps which receives the maximum slowdown versus minimum slowdown

## Slide 22: Scalability
Execution time for GHC to converge
Execution time for XChange-WR market-based technique to converge
# cores | 4 | 32 | 64 | 128 | 256
Cycles | 43 | 484 | 1697 | 6418 | 24903
% interval | 0.87% | 9.69% | 33.95% | 128% | 498%
# cores | 4 | 32 | 64 | 128 | 256
Cycles | 9.47 | 12.49 | 15.89 | 22.64 | 52.70
% interval | 0.19% | 0.25% | 0.32% | 0.45% | 1.05%
(*) Assume 5M cycle reallocation interval
Practical Issues • Evaluations • Conclusions

## Slide 23: Conclusions
Market-based approach very promising
  Fast and scalable
  Solid results
  Adjustable system throughput and fairness
Heuristic approach valid
  Plenty of real-life examples that just work
  Utility models captures application behavior well
  First welfare theorem has weak conditions
  We have reasonable fallback mechanism
Practical Issues • Evaluations • Conclusions

## Slide 24: XChange: A Market-based Approach to Scalable Dynamic Multi-resource Allocation in Multicore Architectures
Xiaodong Wang
José F. Martínez
Computer Systems Lab
Cornell University

## Slide 25: Backup slides

## Slide 26: Prior art: example of non-convexity
mcf’s IPC vs. cache allocation
Chart: mcf
| 1-way | 2-way | 3-way | 4-way | 6-way | 8-way | 12-way | 16-way
IPC | 0.049944 | 0.049975 | 0.049987 | 0.04999 | 0.050008 | 0.050012 | 0.20178 | 0.20872
MPKI | 167.0839 | 166.9625 | 166.9213 | 166.9039 | 166.8352 | 166.8182 | 1.8172 | 0.26198

## Slide 27: Prior art
Key： Performance modeling + resource allocation
Sampling + hill climbing [Choi and Yeung 2006]
Predictive model + hill climbing
  Artificial neural network [Bitirgen et al. 2008]
  Analytical model [Chen and John 2011]
Curve-fitting + elasticity-proportional (Zahedi and Lee 2014)
  Guarantee game-theoretic fairness at the cost of efficiency

## Slide 28: A more sophisticated player model
Compute phase
  Power: assume compute phase is linear to frequency
Measured
(perf. counters)
Miftakhutdinov

## Slide 29: Implementation
Leverage Linux’s APIC timer interrupt
  Every 1 ms, for kernel statistics update
  Designate “master core” to post prices, collect bids
Modest hardware overhead
  ~ 4 kB/core (mostly UMON)

## Slide 30: Bidding strategy
“Guided” hill-climbing
  Tries to go around cache non-convexity issue
  Purchase minimum frequency allocation (800 MHz)
  Bid all remaining money to cache
  Progressively trade off cache ways for power
  Caveat: works only when one resource is non-concave
Chart: 
| 1-way | 2-way | 3-way | 4-way | 6-way | 8-way | 12-way | 16-way
 | 0.049932 | 0.049964 | 0.049975 | 0.049978 | 0.049995 | 0.049997 | 0.1998 | 0.20644

## Slide 31: System throughput (weighted speedup)
13.62%
18.30%
Notes: before start explaining results, need to say assuming zero overhead in calculating operating point.
looking at quality of outcome w/o
scalability: actually coded the overhead in the simulator infrastructure
----- Meeting Notes (2/3/15 18:38) -----
title, axis and legend
a horizontal line of 100%
save time by not saying this

## Slide 32: System fairness (maxmin slowdown)
2.24
2.88
3.23
Notes: ----- Meeting Notes (2/3/15 18:38) -----
bar to number straight line
what is slowdown ratio
why lower is better

## Slide 33: System performance (harmonic speedup)
24%