## Slide 1: SWAP: Effective fine-grain management of shared last-level caches with minimum hardware support
Xiaodong Wang, Shuang Chen, Jeff Setter,
and José F. Martínez
Computer Systems Lab
Cornell University

## Slide 3: Motivation
IBM Blue Gene/Q
Source: IBM
Shared cache
Motivation • Background
Notes: Last-level cache, which occupies almost 50% of the chip area, is an important shared resources in chip-multiprocessors. In this IBM blue gene/Q processor, there are 18 cores sharing the L2 cache, where the interferences among the cores can be high that hurt system performance. We also observed a trend that the number of cores increases, which exerts even higher pressure to the shared cache.

## Slide 4: Motivation
Cavium ThunderX® 48-core CMP
Source: Cavium
Motivation • Background
Notes: Therefore, intelligently manage the shared last-level cache is important to optimize system performance.

## Slide 5: Motivation
Last-level cache is critical to system performance
  ~50% chip area
Performance isolation in shared cache
  Improve system throughput
  Guarantee QoS of latency-critical
  workloads
  Eliminate timing channels
Core
Private cache
Shared last-level cache
Core
Private cache
Core
Private cache
Motivation • Background
Notes: Performance isolation, where the shared cache is partitioned among the co-running applications to eliminate interferences, is desirable xxx

## Slide 6: Background
Cache way partition
  Assign different cache ways to different cores
  Perfect isolation
  Readily available in existing CPUs
  Low repartition overhead
Core
Core
Core
Core
Shared last-level cache
Motivation • Background • SWAP
Coarse-grained
  16 cache ways in ThunderX 48-core processor
Associativity lost
Shared last-level
cache

## Slide 7: Background
Page coloring
  Assign different cache sets to different cores
  Perfect isolation
  OS-level software technique
Core
Core
Core
Core
Shared last-level
cache
Shared last-level
cache
Motivation • Background • SWAP

## Slide 8: Background
Page coloring
  Assign different cache sets to different cores
  Perfect isolation
  OS-level software technique
OS
HW
Physical address
Motivation • Background • SWAP
  High repartition overhead
  Coarse-grained: the number of page colors is limited
    4 color bits, 16 colors in ThunderX 48-core processor

## Slide 9: Background
Fine-grained cache partitioning [1, 2, 3, 4]
  Probabilistically guarantee the size of partitions at the granularity of cache lines
  Requires non-trivial hardware changes
  No clear boundary across partitions: isolation is not strict
[1] Xie and Loh, ISCA’ 09
[2] Sanchez and Kozyrakis, ISCA’ 11
[3] Manikantan et al., ISCA’ 12
[4] Wang and Chen, MICRO’ 14
Motivation • Background • SWAP

## Slide 10: Comparison of schemes
Way
partitioning
Page
coloring
Probabilistic
partitioning
SWAP
Fine-grain
Perfect isolation
Hardware
overhead
Real system
Repartition
overhead
Yes
Yes
Yes
Low
Yes
Yes
Yes
Yes
Probabilistic
Low
Low
Low
Yes
No
No
No
No
High
No
High
Median
Motivation • Background • SWAP
Notes: Color blind

## Slide 11: SWAP: Set and WAy Partitioning
Way partitioning vertically divides the cache
  16 cache ways in ThunderX for 48 cores
Page coloring horizontally divides the cache
  16 page colors in ThunderX for 48 cores
Combine way partitioning and page coloring
Background • SWAP • Evaluation

## Slide 12: SWAP: Set and WAy Partitioning
Combine way partitioning and page coloring
  Divide the cache in a 2-dimensional manner
  Maximum 256 partitions w/ 16 cache ways and 16 page colors, fine-grained enough for 48 cores
Background • SWAP • Evaluation

## Slide 13: SWAP: Set and WAy Partitioning
Contribution
  Combine way partitioning and page coloring that enables fine-grain cache partition in real systems
Challenges
  What’s the shape of the partition?
  How are partitions placed with each other?
  How to minimize repartition overhead?
Background • SWAP • Evaluation

## Slide 14: SWAP: Set and WAy Partitioning
Partition shape
  Given the partition size, how many cache ways and pages colors should the partition have?
Background • SWAP • Evaluation
Partition size = 18
# cache way
# page color
3
6
2
6
9
9
3
2

## Slide 15: SWAP: Set and WAy Partitioning
Partition Placement
  Partitions do not overlap (interference-free)
  No cache space is wasted
Background • SWAP • Evaluation

## Slide 16: SWAP: Set and WAy Partitioning
Partition shape
  Partitions cannot simply expand to occupy unused area
Background • SWAP • Evaluation

## Slide 17: SWAP: Set and WAy Partitioning
Partition shape
  Given the partition size, we classify the partitions into different categories
  Page colors unchanged if the partition size stays within a certain range
  Partitions aligned with each other
Partition size
# page color
Category
…
…
…
Cache capacity = S, number of page colors = K
Cavium ThunderX® 48-core processor:
Cache capacity = 256 (16 MB), number of page colors = 16
P1
P2
P4
P3
P6
P9
P5
P8
P7
Background • SWAP • Evaluation

## Slide 18: SWAP: Set and WAy Partitioning
Partition Placement
  Start with large partitions (with more colors)
  Assign the partition with page colors that have most cache ways left
P1
P3
P2
8 ways
8 page colors
 | Size
P1 | 40
P2 | 12
P3 | 12
usge cntr
0
0
0
0
0
0
0
0
5
5
5
5
5
5
5
5
8
8
8
8
5
5
5
5
8
8
8
8
8
8
8
8
Background • SWAP • Evaluation

## Slide 19: SWAP: Set and WAy Partitioning
Reduce repartition overhead
  Adjust cache way assignment incurs low overhead
    Write way permission register
  Adjust page color assignment is cumbersome
    Migrate the page from the old color to the new color
Background • SWAP • Evaluation

## Slide 20: SWAP: Set and WAy Partitioning
Reduce repartition overhead
  Key: reduce page re-coloring
  Classify the partitions as before
    Same: keep the original colors
    Downgrade: use partial original colors
    Upgrade: may use any colors
  Estimate the cache way usage before placement
Background • SWAP • Evaluation
Notes: Transition is too fast

## Slide 21: SWAP: Set and WAy Partitioning
Reduce repartition overhead
  Classify the partitions as before
  Estimate the cache way usage
P1
P3
P2
8 ways
8 page colors
 | Before | After
P1 | 40 | 8
P2 | 12 | 8
P3 | 12 | 48
usge cntr
0
0
0
0
0
0
0
0
Up
Down
P3’
8x6
P2’
4x2
P1’
4x2
2
2
2
2
0
0
0
0
3
3
3
3
1
1
1
1
Background • SWAP • Evaluation

## Slide 22: SWAP: Set and WAy Partitioning
Reduce repartition overhead
  Start with large partitions (with more colors)
  Assign the partition with page colors that have most cache ways left
P1’
P2’
8 ways
8 page colors
 | Before | After
P1 | 40 | 8
P2 | 12 | 8
P3 | 12 | 48
usge cntr
3
3
3
3
1
1
1
1
Up
Down
P3’
9
9
9
9
7
7
7
7
8
8
8
8
8
8
8
8
Background • SWAP • Evaluation

## Slide 23: Other issues
Cache miss-ratio curve
  Profiling
Lookahead algorithm [1] decides partition sizes
Other issues
  Hashed indexing
  Superpage
[1] Qureshi and Patt, MICRO’ 06
Background • SWAP • Evaluation

## Slide 24: Experimental setup
Cavium ThunderX Processor
  48-core CMP, 1.9GHz
  16MB shared last-level cache
  64GB DDR4-2133, 4 channels
  Ubuntu Linux 3.18
Performance analysis
  Mix of SPEC2000 and SPEC2006 multi-programed workloads
  Latency critical workload memcached
SWAP • Evaluations • Conclusions
Notes: Partition L2 cache based on cache ways. Essentially, other cache allocation techniques, such as z-cache, vantage essentially mimic high associativity with limited physical cache ways. There is no fundamental reason that we cannot use it.
not really a limitation: essentially z-cache does the same thing
640W thing: IBM Power8 12 core: 200-250W @ 22nm
Intel Haswell: 155W@ 22nm
The results doesn’t depend on the absolute number.
The actual cache partition is orthogonal to our proposal.

## Slide 25: Static partitioning
48-app
12.5%
Running application bundle
SWAP • Evaluations • Conclusions
Notes: Baseline: unmanaged, shared cache

## Slide 26: Dynamic partitioning
Running application sequence
  The next application in the sequence replaces the finished one; cache partitions change dynamically
SWAP • Evaluations • Conclusions

## Slide 27: Dynamic partitioning
Running application sequence
  The next application in the sequence replaces the finished one; cache partitions change dynamically
Cores | Seq | WAY | SET | SWAP | Avg. Inj interval
 | 1 | 1.04x | 1.02x | 1.08x | 46s
 | 2 | 1.11x | 1.04x | 1.17x | 41s
 | 1 | 0.97x | 1.04x | 1.11x | 31s
 | 2 | 1.04x | 1.02x | 1.20x | 25s
 | 1 | 0.92x | 0.99x | 1.11x | 34s
 | 2 | 1.00x | 1.03x | 1.15x | 25s
16
32
48
SWAP • Evaluations • Conclusions

## Slide 28: Guarantee QoS
Latency workload memcached co-located with background multi-programmed workloads
Shared cache
SWAP
SWAP • Evaluations • Conclusions
Notes: Cache exploration or phase changes of the background workloads

## Slide 29: Guarantee QoS
Latency workload memcached co-located with background multi-programmed workloads
16-app SPEC bundle
8.1%
SWAP • Evaluations • Conclusions

## Slide 30: Conclusions
A real system implementation of fine-grain cache partitioning in large CMP systems
  Combine cache way partitioning and page coloring
  Delivers superior system throughput
  Guarantee QoS of latency-critical workloads
SWAP • Evaluation • Conclusions

## Slide 31: SWAP: Effective Fine-Grain Management of Shared Last-Level Caches with Minimum Hardware Support
Xiaodong Wang, Shuang Chen, Jeff Setter,
and José F. Martínez
Computer Systems Lab
Cornell University

## Slide 32: Static partitioning
16-core
24-core
32-core
48-core
13.9%
14.1%
12.5%
12.5%