## Slide 1: SecDCP: Secure Dynamic Cache Partitioning for Efficient Timing Channel Protection
Yao Wang, Andrew Ferraiuolo, Danfeng Zhang, Andrew C. Myers, and G. Edward Suh
Cornell University, Penn State University

## Slide 2: Cache Timing Channel Problem
What is a timing channel?
Caches are vulnerable to timing channel attacks
  Timing difference
    Cache misses take much longer than cache hits
  Interference
    One process can evict the cache lines of another process
# Example code:
if (secret)
sleep(10s)
else
sleep(5s)
Victim’s
secret
Attacker’s
timing
affects
infers
Cloud
Mobile
Notes: Mention the goal of this paper is to propose a cache timing channel protection scheme.
Mention we target at attacks that exploits interference between processes
Put less stress on mobile devices (may be able to steal information through cache timing channels)

## Slide 3: Cache Side Channel Attacks on AES
Attacker loads the cache
AES program accesses AES table entries
  Index = key plaintext
Attacker probes the cache
  Derive index and plaintext
  Infer the key
core 0
AES
core 1
Attacker
Shared cache
Memory
Addresses of cache accesses
can leak information!
28

## Slide 4: Cache Covert Channel Attacks
core 0
Attacker 0
core 1
Attacker 1
Shared cache
Memory
Attacker 1 loads the cache
To send a bit ‘0’, Attacker 0 does not access the cache
  Attacker 1 gets cache hits
To send a bit ‘1’, Attacker 0 sends a bunch of accesses
  Attacker 1 gets many cache misses
Number of cache accesses
can also leak information!

## Slide 5: Previous Approaches
Randomization-based techniques
  Idea: randomize the cache mapping
  Con: do not hide number of cache accesses
Partitioning-based techniques
  Idea: statically divide the cache into multiple partitions
  Con: incur high performance overhead
Dynamic cache partitioning
  Utility-based partitioning, Vantage, PIPP, etc
  Con: insecure
Secure dynamic
cache partitioning?
cache
0x0000
0x0080
cache

## Slide 6: Hierarchical Security Policy
…
Security class
A
B
…
C
…
Tier N
Tier 2
Tier 1
A
B
A
C
Implication 1
Banking
Medical
Implication 2
Banking
Game
Unidirectional Protection!

## Slide 7: SecDCP: Secure Dynamic Cache Partitioning
Key idea: use the runtime cache demand of public applications to guide dynamic cache partitioning
Two components
  Partitioning Allocation Algorithm (PAA)
    Determines the size of each partition
  Partition Enforcement Mechanism (PEM)
    Enforces the new partition size set by PAA
PAA
Cache
Monitoring
PEM
New partition size
Adjust partition size
In each time
period T

## Slide 8: Partition Allocation Algorithm (PAA)
We use utility monitors (UMON) [1] to monitor the runtime cache demand
  Generate miss rate curve for L program
H
L
[1] Moinuddin Qureshi and Yale Patt, “Utility-based partitioning, a low-overhead, high-performance, runtime mechanism to partition shared caches”, MICRO 2006
gain = MR(X) – MR(X+1)
loss = MR(X–1) – MR(X)
20%
X: Current number of cache ways for L
Notes: PAA dedicates at least one cache way to each program
Reason why this is good for performance. Performance increase will be significant (given th_inc), performance loss will be bounded (given th_dec).
If you want, you can further improve the thresholds. We found 20% works pretty well across all the benchmarks
Only L program’s demand is used to decide the new partition

## Slide 9: Partition Enforcement Mechanism (PEM)
Naïve approach: flush the adjusted cache ways
Our approach
  L’s partition increases
    Does not flush the adjusted cache ways
    Information flow from L to H is benign
  L’s partition decreases
    Only flushes the cache lines that belong to L
    Prevent information flow from H to L
Shared cache
Shared cache
L: 2 cache ways
H: 2 cache ways
L: 3 cache ways
H: 1 cache way
Notes: When increase, we do not flush, so that H program can continue to get cache hits on these cache lines
When decrease, if you don’t flush L’ cache lines, L can see its cache lines be evicted by H program later. Focus on what L sees

## Slide 10: Evaluation Methodology
Simulator
  gem5
Benchmarks
  SPEC CPU2006
core
$L1
$L2
core
$L1
Memory
2/4
32kB
2-way
1MB, 8-way /
2MB, 16-way
200-cycle latency,
8GB/s
cache-insensitive | astar, libquantum, gobmk, h264ref, hmmer, sjeng
cache-sensitive | bzip2, mcf, soplex, xalan

## Slide 11: Performance for Two-Core System
SecDCP achieves similar performance as LRU and utility-based partitioning
secure
insecure
20% threshold
Notes: - Performance gain up to 40% for some benchmarks

## Slide 12: Sensitivity Study: Different Threshold Values
Optimal threshold value varies with workloads
20% threshold works reasonably well for diverse workloads (within 5% of the optimal threshold)
Notes: Threshold has noticeable impact on certain workloads.
20% threshold generally works well for diverse workloads, within 5% of the optimal threshold

## Slide 13: Summary
We proposed SecDCP, a secure dynamic cache partitioning technique to defend against timing channel attacks
Key idea: exploit the asymmetry in the security policy to enable dynamic cache partitioning
Main take-away: dynamic cache partitioning can be performed securely and improve the performance under asymmetric security policies.

## Slide 14: Backup slides

## Slide 15: PAA under General Security Policy
Case 1: L1 , M1 , M2
  Wrong design: allocate one cache way from M1 to L1 based on runtime demand
  Illegal information flow from M1 to M2
  Solution: round-robin arbitration
Case 2: M1 , M2
  Wrong design: M1 take cache ways from H without any restriction
  Illegal information flow from M1 to M2
  Solution: reserve cache ways for each lower security class
PAA decides the action
for each security class
Increase:
Decrease:
Keep:
H’s cache ways
0
1
2
3
M1
M2
Notes: More details in the paper

## Slide 16: Ratio of Different Phase Combinations

## Slide 17: Performance for SI workloads

## Slide 18: Performance for II workloads

## Slide 19: Efficiency Discussion
Applications show different phases
  S: cache-sensitive phase
  I : cache-insensitive phase
Case analysis for (PublicApp, SensitiveApp)
  (I, I): Partition does not matter much
  (I, S): SecDCP allocates most of cache to SensitiveApp
  (S, I): Depends on threshold value
  (S, S): Depends on threshold value

## Slide 20: Different Security Policies
Chart: 
| Weighted Speedup
Static | 100
SecDCP | 107
LRU | 109
App4
App3
App2
App1
Linear Security Policy
App4
App3
App2
App1
Mobile Security Policy
Chart: 
| Weighted Speedup
Static | 100
SecDCP | 103
LRU | 105
Notes: In mobile security policy, the baseline’s performance improves by allowing app1 and app2 to share a cache partition