## Slide 1: Secure Dynamic Memory Scheduling against Timing Channel Attacks
Yao Wang, Benjamin Wu, G. Edward Suh
Cornell University

## Slide 2: Timing Channel Problem
What is a timing channel?
Why do we care?
  Attacks demonstrated in real world environment
    Example: cache timing channel attacks in Amazon EC21,2
  Capabilities
    Steal cryptographic keys, predict users’ passwords, track users’ browser visit history, etc.
# Example code:
if (secret)
sleep(10s)
else
sleep(5s)
Victim
Secret
Timing
Attacker
affects
infers
[1] Thomas Ristenpart, Eran Tromer, Hovav Shacham and Stefan Savage, “Hey, You, Get Off of My Cloud: Exploring Information Leakage in Third-Party
Compute Clouds”, CCS09
[2] Yinqian Zhang, Ari Juels, Michael Reiter and Thomas Ristenpart, “Cross-VM Side Channels and Their Use to Extract Private Keys”, CCS12

## Slide 3: Timing Channels in Main Memory
DRAM
Memory Controller
Security Domain (SD)
SD0
SD1
Time
req
SD0
req
SD1
Rank 0
Rank 1
Banks
req
req
Different ranks: Trank
req
req
Different banks in the same rank: Tbank
req
req
The same bank in the same rank: Tworst
DRAM Schedule
DRAM timing constraints
Trank < Tbank < Tworst
6 18 43

## Slide 4: A Covert Channel Attack1
Sender sends a sequence of bits by dynamically changing memory demand
  To send a ‘0’, sender does not issue any memory request
  To send a ‘1’, sender sends many memory requests
Receiver keeps sending requests
  Measures its own throughput
  Throughput variations
Core 1
Core 2
Memory
Sender
Receiver
$L1
$L1
1 0 0 1 0 1 1 0
[1] Yao Wang, Andrew Ferraiuolo, and Edward Suh, “Timing Channel Protection for a Shared Memory Controller”, HPCA 2014.

## Slide 5: Naïve Protection: Temporal Partitioning (TP)1
Static turn scheduling
Add dead time at the end of each turn
  No new memory transactions can be issued during dead time
  Tdead >= Tworst (43 cycles)
[1] Yao Wang, Andrew Ferraiuolo, and Edward Suh, “Timing Channel Protection for a Shared Memory Controller”, HPCA 2014.
Time
SD0
SD1
SDN
Turn
Time
Turn
Tdead
Dead time introduces significant performance overhead!

## Slide 6: Reducing Dead Time Overhead
Spatial partitioning1,2
  Map security domains to different banks or ranks
  Pro:
    Significantly reduce dead time
  Cons:
    Scalability issue
    Memory fragmentation
    Requires OS support
Bank Triple Alternation (BTA)2
  Enforce consecutive turns to access different banks
  Pro:
    Does not require spatial partitioning
  Con:
    Inefficient scheduling
Tbank (or Trank)
[1] Yao Wang, Andrew Ferraiuolo, and Edward Suh, “Timing Channel Protection for a Shared Memory Controller”, HPCA 2014.
[2] Ali Shafiee, Akhila Gundu, Manjunath Shevgoor, Rajeev Balasubramonian and Mohit Tiwari, “Avoiding Information Leakage in the Memory Controller
with Fixed Service Policies”, MICRO 2015
Time
Turn
Tbank
Time
Turn
Bank 0,3,6
Bank 1,4,7
Bank 2,5

## Slide 7: Secure Memory Scheduling: SecMC-NI
Key idea: interleaving requests that access different ranks and banks to construct an efficient schedule
Parameter Definition
  Trank : 6 cycles
  Tbank :18 cycles
  Tworst: 43 cycles
  Tturn : Turn length
Time
SD0
SD1
SDN
Turn

## Slide 8: Interleaving Requests that Access Different Banks
Request reordering algorithm
  Reorder the requests so that requests that access the same bank are separated by at least Tturn cycles
Request selection algorithm
  Requests in a turn must access different banks
  At most Tturn/Tbank requests are scheduled in each turn
  Example: Tturn = 54 cycles
Effect of reordering
Notes: This is secure

## Slide 9: Can We Do the Same for Ranks?
Rank 0
Rank 3
Rank 2
For each rank, construct the previous schedule separately
  At most Tbank/Trank ranks are selected in each turn
Combine them by shifting each rank schedule by Trank cycles
  Example: Tturn = 54 cycles
At most 9 requests can be issued in each turn !

## Slide 10: Performance Evaluation
Simulator
  ZSim + DRAMSim2
Workloads
  Multi-program workloads using SPEC CPU2006 benchmarks
Performance metric
  Weighted speedup
core
$L1
$L2
core
$L1
Memory
8
32kB
8MB
1 memory channel, 8 ranks,
8 banks in each rank

## Slide 11: Comparison with BTA
SecMC-NI outperforms BTA by 45% on average
SecMC-NI cuts the average queuing delay of BTA by half
Weighted Speedup (Normalized to FR-FCFS)
Queuing Delay
Notes: We show one program with eight copies to study the impact of memory intensity
Also study mixed workloads

## Slide 12: Comparison with Spatial Partitioning
SecMC-NI achieves similar performance as BP (Bank Partitioning) on average
But there is still a significant performance gap (35%) between SecMC-NI and RP (Rank Partitioning)
Can we do better?
Notes: We show one program with eight copies to study the impact of memory intensity
Also study mixed workloads

## Slide 13: Trade Security for Performance: SecMC-Bound
Key idea:
  For performance: allow dynamic memory scheduling (like FR-FCFS)
  For security: enforce each request to return at pre-determined time
Can we find the worst-case finish time for a request?
  TP with 2-core case, turn length 43 cycles
R0B0
SD0
DRAM
Time
Interference from
other domains
Finish
Finish
Worst-case
finish time
Time
SD0
req_0
SD1
req_0
SD0
req_1
SD1
req_1
43
Under TP, the i th request from
security domain s can finish by
s*43 + i*43*num_domains+ 43
Return
Notes: Of course we don’t want to return at TP’s time

## Slide 14: Return Earlier than Worst-Case Time
For each request, we assign
  Expected Issue time (EI) : used for arbitration
    Parameter b: interval between EIs
    The request with the smallest EI wins the arbitration
  Expected Response time (ER) : used for security
    Parameter d: delay between EI and ER
    As long as every request returns at ER, no information leaks
      d hides the interference between different security domains
Time
SD0
req_0
SD1
req_0
b
SD1
req_0
ER
d
What if a request
finishes after its ER?
SD2
req_0
43
43
b
EI
EI
EI
Return

## Slide 15: Limit the Information Leakage of Violations (1)
ER violation: a request finishes after its ER
  ER violations represent information leakage
Limit the information that one violation conveys
  A violation can only have one of W possible delays
Time
req
EI
ER
d
ER + d1
ER + dW-1
ER + dworst
Worst-case time
derived from TP
Finish
Return
Notes: ----- Meeting Notes (9/30/16 15:28) -----
ER VIOLATION
get rid of "a kind"

## Slide 16: Limit the Information Leakage of Violations (2)
Set a limit on the number of violations per security domain
  M violations in every N requests (a period)
    e.g., M = 4, N = 1,000: at most 4 violations can happen in 1000 requests
  Once a security domain reaches the limit
    Always return at the worst-case time derived from TP
    Attacker cannot get further information
  Reset the violation counter after a period
How many bits can an attacker derive in a period?
This is a conservative bound !
Notes: This is conservative bound

## Slide 17: Performance under Different Limits
b = 6, d = 160
As the limit gets lower
  Performance starts to decrease due to entering worst-case mode
  Leakage decreases exponentially
Tradeoff between performance and security

## Slide 18: Comparison with Previous Schemes
SecMC-Bound outperforms SecMC-NI and BP
  Trade security for performance
  The leakage is bounded

## Slide 19: Summary
Shared memory controllers are prone to timing channel attacks
Previous protections suffer from either inflexibility or high performance overhead
SecMC-NI completely removes timing channels while achieving 45% performance improvement over the state of the art (BTA)
SecMC-Bound further improves the performance by enabling a trade-off between security and performance with a quantitative security guarantee

## Slide 20: Backup Slides

## Slide 21: Square and Multiply Algorithm for RSA
C: encrypted message
x: decrypted message
N: product of two large prime numbers
d: RSA private key
n: the number of bits in the key
x = C
for j = 1 to n
x = mod(x2, N)
if dj == 1 then
x = mod(xC, N)
end if
next j
return x
Timing channel

## Slide 22: Optimization: Dynamic Tuning of b and d Values
Intuition: with fixed b and d values, less memory-intensive programs incur less ER violations
  Use smaller b and d values for less memory-intensive programs
  Benefit: smaller b and d values reduces memory latency
Dynamic tuning based on observed number of violations
  Assume m is number of violations in previous period (N requests)
    if m <= thdec, d = d – constant
    if m >= thinc, d = d + constant
    else, d = d

## Slide 23: Dynamic Tuning of d Value
Dynamic tuning of d value improves performance by reducing d to a value that just meets the security requirements
  e.g., 160  20
Designers do not need to come up with good d values
Initial d value = 160
thinc = 3
thdec = 0

## Slide 24: Performance Evaluation
ZSim + DRAMSim2
  ZSim: cores, caches
  DRAMSim2: DRAM
8-program workloads
  24 SPEC CPU2006 benchmarks
  Each program fast-forwards for 1 billion instructions and then simulates for 100 million instructions

## Slide 25: SecMC-NI: Effect of Address Randomization
Address randomization benefits hmmer significantly
  Requests are distributed more evenly across banks and ranks

## Slide 26: Parameter Sweep for b and d (No Limit)
Smaller b and d result
in better performance
Smaller b and d result
in more violations
b = 3
b = 6

## Slide 27: Optimization: Avoiding Worst-Case Times
Gradually increase the value of d with the number of violations
Before Optimization
After Optimization

## Slide 28: Parameter Sweep for b and d (no limit)
b = 3
b = 6

## Slide 29: Performance under Different Limits
b = 6, d = 160
As the limit gets lower
  Performance starts to decrease due to entering worst-case mode
  Leakage decreases exponentially
Tradeoff between performance and security

## Slide 30: Dynamic Tuning of d Value
Initial d value = 160
Static

## Slide 31: Comparison with Previous Schemes
SecMC-Bound parameters
  b = 6, d = 160

## Slide 32: Combining SecMC-Bound with Partitioning
Combining SecMC-Bound with spatial partitioning outperforms applying spatial partitioning alone
b = 3
d = 24