## Slide 1: Efficient Timing Channel Protection for On-Chip Networks
Yao Wang and G. Edward Suh
Cornell University

## Slide 2: On-Chip Networks are Shared Resources
Future large-scale multi-cores will be shared among multiple applications / virtual machines
Virtual Machine A
Virtual Machine B
Notes: Figures – Processor picutres / Mesh NoC / cloud computing – virtual machines
To fully utilize the many-core system, parallel workloads are running concurrently
They share resources such as caches ($L2), On-chip network, memory controller, etc
The on-chip network is shared by different applications to deliver traffic, which causes interference between each other
Cloud computing

## Slide 3: Problem: Timing Channels
Shared NoC causes interference
Virtual Machine A
Virtual Machine B
Network interference introduces timing channels
  Side channel
  Covert channel
High assurance systems requires security guarantee
  Example: Corporate virtual machines on the cloud
Notes: The latency and throughput variations from network interference form timing channels which can be utilized to extract information.
These are often called side channel or covert channel attacks. These attacks can result in the leakage of critical information
Why is this an important problem
  Point out examples: high assurance (corcoporate VMs, military, flight control? …
In high assurance systems, these timing channels should be eliminated to provide security guarantee.
  Cloud computing running multiple virtual machines on the same hardware (trade secret, customer profiles, etc)

## Slide 4: RSA Example
RSA : a public key cryptographic algorithm
  Prone to timing channel attacks
Core 0
MC 0
Core 1
MC 1
Core 2
MC 2
Crossbar
RSA
Attacker
key: 0110…

## Slide 5: RSA Example
RSA : a public key cryptographic algorithm
  Prone to timing channel attacks

## Slide 6: Outline
Objective: Eliminate timing channels through the shared on-chip networks
  Completely eliminate information leakage
  Low performance overhead
Rest of the talk
  Potential approaches
  Our solution
  Evaluation
  Related work
  Conclusion

## Slide 7: Use Quality-of-Service?
QoS techniques provide performance isolation to different network flows
QoS techniques are not enough for security
  A flow can use bandwidth beyond its allocation
  Bandwidth utilization reveals the flow demand
Flow A Demand | Flow B Demand | Flow A BW utilization
100% | 100% | 
100% | 0% | 
1
2
A
B
Bandwidth allocation
A: 50%
B: 50%
50%
100%

## Slide 8: Static Partitioning
To eliminate timing channels, resource allocation cannot depend on run-time demands
Static partitioning
  Spatial Network Partitioning (SNP)
  Temporal Network Partitioning (TNP)
Completely eliminate the timing channels
  High performance overhead
SNP
TNP
Cycle 0
Cycle 1
…
VM A
VM A
VM B
VM B

## Slide 9: One-Way Information Leak Protection
Usually only one-way information protection is needed
  Multi-level security (MLS) model
One-way protection is the key for efficient timing channel protection
Personal APP
(Music Player)
Business App
(Bank Management)
Regular VM
Corporate VM
Low-Security Domain
High-Security Domain
Information
flow
PC
Cloud Computing
In general
Notes: Figure (multiple levels of security, which information flows are allowed and which are not)
Multi-level security model (MLS), security domains
Usually only one-way information protection is needed, from high-security domain to low-security domain
This property is crucial to provide efficient timing channel protection

## Slide 10: Timing Channel through NoC
HS demand
0
1
1
LS throughput
HS: High-Security Domain
LS: Low-Security Domain
HS ---> LS
Notes: Dependency curve
  HS  LS
  Performance of LS domain changes w/ demands from HS
LS doman’s communication latency / throughput should not be impacted by HS domain communications

## Slide 11: Reversed Priority with Static Limits (RPSL)
Reversed Priority
  Assign high priority to low-security domain
  The behavior (throughput, latency) of low-security domain is not affected by high-security domain
Static Limits
  Low-security domain could initialize Denial-of-Service (DoS) attack
  Static limit controls the amount of traffic that low-security domain can send during a certain interval
Notes: Firetruck example
Basic idea: assign high priority to low-security traffic so that its behavior is not affected by the dynamic variation of the high-security traffic

## Slide 12: Implementation: Avoid Interference
Priority-based separable allocator
  Input arbiter & Output arbiter
Static virtual channel allocation
  Avoid head-of-line blocking
Router
Virtual Channels
Input link
0
1
2
3
Low-security Domain
High-security Domain

## Slide 13: Implementation: Avoid DoS
Static limit control mechanism
  Counter & Control logic
Apply to both input and output arbiter
Priority-based Arbiter
Counter
Requests
Winning
Request
Static limit Control
Low-security Domain
High-security Domain
Input Arbiter

## Slide 14: Benefits of One-Way Protection
Time
BW
Utilization
Total BW
HS
LS
Round-robin Allocator
LS
HS
Time
BW
Utilization
Total BW
HS
LS
Temporal Network Partitioning
LS
HS
Time
BW
Utilization
Total BW
HS
LS
LS
HS
RPSL
1
2
LS
HS

## Slide 15: Experimental Setup
Goals of experiments
  Timing channel protection
  DoS protection
  Performance overhead
Darsim: cycle-level NoC simulator
Comparison of three schemes
  Round-robin allocator (ISLIP)
  Temporal Network Partitioning (TNP)
  Reversed Priority with Static Limits (RPSL)

## Slide 16: Timing Channel: No Protection
Simple network
Round-robin allocator
1
2
3
4
Low-security Domain
High-security Domain
HS
LS
Notes: Simple example using TNP and RPSL (Figure)
Prove the effectiveness of both schemes

## Slide 17: Timing Channel: Two-way Protection
Simple network
Temporal Network Partitioning
1
2
3
4
Low-security Domain
High-security Domain
HS
LS
0.4/1.0
Notes: Simple example using TNP and RPSL (Figure)
Prove the effectiveness of both schemes

## Slide 18: Timing Channel: One-way Protection
Simple network
Reversed Priority with Static Limits (Static limit = 0.8)
1
2
3
4
Low-security Domain
High-security Domain
HS
LS
1.0/1.0
Notes: Simple example using TNP and RPSL (Figure)
Prove the effectiveness of both schemes

## Slide 19: Performance
Applications show bursty traffic
RPSL is efficient for bursty traffic
HIGH
LOW

## Slide 20: Related Work
Side-channel protection
  Shared resources are prone to side-channel attacks, e.g. shared caches, branch prediction
  Cannot be applied to NoC
QoS schemes
  Allows resource usage beyond allocation
  Insufficient to prevent timing channel attacks
Composability
  Remove interference between applications for fast integration
  Require bi-directional non-interference, incur high performance overhead

## Slide 21: Conclusion
Shared on-chip networks introduce timing channels
  Prevent effective sharing of large-scale NoC in high assurance systems
One-way timing channel protection is sufficient in many situations
RPSL provides efficient one-way timing channel protection
  Incurs low performance overhead

## Slide 22: Extend to Multiple Domains

## Slide 23: Denial-of-Service Protection (RPSL)
Simple network
1
2
3
4
Low-security Domain
High-security Domain
HS
LS
Static Limit on LS
Static Limit on LS

## Slide 24: Synthetic Traffic Patterns
6-by-6 mesh network
Two security domains
Transpose traffic
Round-robin
Temporal Network Partitioning
RPSL
HIGH
LOW
LS offered BW
LS offered BW
LS offered BW

## Slide 25: Synthetic Traffic Patterns
6-by-6 mesh network
Two security domains
Hotspot Traffic
HIGH
LOW
Round-robin
Temporal Network Partitioning
RPSL