## Slide 1
Experimental Evaluation
SecDCP Overview
SecDCP: Secure Dynamic Cache Partitioning for Efficient Timing Channel Protection
Yao Wang, Andrew Ferraiuolo, Danfeng Zhang*, Andrew C. Myers, and G. Edward Suh
Computer Systems Laboratory, Electrical and Computer Engineering, Cornell University, Ithaca, NY
*Computer Science and Engineering, Penn State University, University Park, PA
Exploits the asymmetry in the security policy to enable dynamic cache partitioning
Supports a general security policy
Defeats timing channel attacks while improving the performance compared to previous approaches
Take-away: dynamic cache partitioning can be performed securely and improve performance under asymmetric security policies
Example Attack
Threat Model
Timing channels introduce serious security threats in modern computing systems.
Shared caches are vulnerable to timing channel attacks due to interference among concurrently running applications.
Use gem5 simulator to evaluate performance
Multi-program workloads constructed from SPEC CPU2006
Left: Performance comparison among four cache schemes
Right: Performance impact of different threshold values
Victim’s
secret
Attacker’s
timing
affects
infers
Randomization-based techniques
        - Idea: randomize the cache mapping
        - Con: do not hide the number of accesses
Partition-based techniques
- Idea: statically divide the cache into multiple partitions
- Con: incur high performance overhead
core 0
Attacker 0
core 1
Attacker 1
Shared cache
Memory
Hierarchical Security Policy
Security Implications
Target Platforms
Cloud
Mobile
Attacker 1 loads the cache
To send a bit ‘0’, Attacker 0 does not access the cache
- Attacker 1 gets cache hits
To send a bit ‘1’, Attacker 0 sends a bunch of accesses
- Attacker 1 gets cache misses
…
Security class
A
B
C
Tier N
Tier 2
Tier 1
Implication 1
Banking
Medical
Implication 2
Banking
Game
A
B
A
C
Number of cache accesses leaks information!
…
…
SecDCP Implementation
Key idea: use the runtime demand
of public applications to guide dynamic
cache partitioning
Two components:
PAA
Cache
Monitoring
PEM
New partition size
Adjust partition size
In each time period T
        Partitioning Allocation Algorithm (PAA)
        - Determines the size of each partition
Partition Enforcement Mechanism (PEM)
    - Enforces the new partition size
High-Level Structure
PAA
PEM
Use utility monitors (UMON) to monitor the runtime cache demand
gain = MR(X) – MR(X+1)
loss = MR(X-1) – MR(X)
X: current number of cache ways for L
H
L
PAA decides the action
for each security class
Increase:
Decrease:
Keep:
Case 1: L1 , M1 , M2
Wrong design: allocate one cache way from M1 to L1
based on runtime demand
Illegal information flow from M1 to M2
Solution: round-robin arbitration
Case 2: M1 , M2
Wrong design: M1 takes cache ways from H without any restriction
Illegal information flow from M1 to M2
Solution: reserve cache ways for each lower security class
H’s cache ways
0
1
2
3
M1
M2
Shared cache
Shared cache
Simple policy
General policy
20%
L: 2 cache ways
H: 2 cache ways
L: 3 cache ways
H: 1 cache way
L’s partition increases
Does not flush the adjusted cache ways
Information flow from L to H is benign
L’s partition decreases
Only flushes the cache lines that belong to L
Prevents information flow from H to L
Problem
Previous Approaches
Our approach (SecDCP)